ANNEXURE I : STREAMFLOW CALIBRATIONS

I.1.	Calibration at Gauge CG25	2

I.2.	Calibration at Gauge CG26	6

I.3.	Calibration at Gauge CG50	10

I.4.	Calibration at Gauge CG55	14

I.5.	Calibration at Gauge MG19	18

I.6.	Calibration at Gauge MG23	22

# Calibration at Gauge CG25

## Statistics of simulated and observed sequences

| Index | Unit | Observed | Simulated |
| --- | --- | --- | --- |
| Mean annual runoff (MAR) | (Million m3) | 130.82 | 130.60 |
| Standard deviation of annual flows (S) | (Million m3/yr) | 77.90 | 84.87 |
| Coefficient of variability (S/MAR) | (%) | 59.55 | 64.98 |
| Coefficient of skewness | - | 0.7765 | 0.9114 |
| Range | (% MAR) | 537.37 | 395.09 |
| Autocorrelation coefficient of annual flows | - | 0.3352 | 0.2226 |
| Mean of logs of annual flows | (Million m3) | 2.0351 | 2.0099 |
| Standard deviation of logs of annual flows | - | 0.2824 | 0.3379 |
| Index of seasonal variability | (%) | 32.10 | 28.52 |

## Observed versus simulated streamflow (monthly)

## Observed versus simulated streamflow (annual)

## Monthly streamflow histogram

## Observed versus simulated flow scatter diagram

## Monthly streamflow cumulative frequency curve

## Seasonality of flows

# Calibration at Gauge CG26

## Statistics of simulated and observed sequences

| Index | Unit | Observed | Simulated |
| --- | --- | --- | --- |
| Mean annual runoff (MAR) | (Million m3) | 37.82 | 37.03 |
| Standard deviation of annual flows (S) | (Million m3/yr) | 19.06 | 20.56 |
| Coefficient of variability (S/MAR) | (%) | 50.40 | 55.51 |
| Coefficient of skewness | - | 0.5254 | 0.6638 |
| Range | (% MAR) | 357.00 | 315.92 |
| Autocorrelation coefficient of annual flows | - | 0.2448 | 0.0807 |
| Mean of logs of annual flows | (Million m3) | 1.5167 | 1.4955 |
| Standard deviation of logs of annual flows | - | 0.2457 | 0.2693 |
| Index of seasonal variability | (%) | 31.53 | 29.19 |

## Observed versus simulated streamflow (monthly)

## Observed versus simulated streamflow (annual)

## Monthly streamflow histogram

## Observed versus simulated flow scatter diagram

## Monthly streamflow cumulative frequency curve

## Seasonality of flows

# Calibration at Gauge CG50

## Statistics of simulated and observed sequences

| Index | Unit | Observed | Simulated |
| --- | --- | --- | --- |
| Mean annual runoff (MAR) | (Million m3) | 80.70 | 81.15 |
| Standard deviation of annual flows (S) | (Million m3/yr) | 38.49 | 40.603 |
| Coefficient of variability (S/MAR) | (%) | 47.70 | 50.03 |
| Coefficient of skewness | - | 0.8555 | 0.8965 |
| Range | (% MAR) | 257.75 | 303.15 |
| Autocorrelation coefficient of annual flows | - | 0.1419 | 0.1650 |
| Mean of logs of annual flows | (Million m3) | 1.8582 | 1.8555 |
| Standard deviation of logs of annual flows | - | 0.2180 | 0.2292 |
| Index of seasonal variability | (%) | 26.77 | 25.22 |

## Observed versus simulated streamflow (monthly)

## Observed versus simulated streamflow (annual)

## Monthly streamflow histogram

## Observed versus simulated flow scatter diagram

## Monthly streamflow cumulative frequency curve

## Seasonality of flows

# Calibration at Gauge CG55

## Statistics of simulated and observed sequences

| Index | Unit | Observed | Simulated |
| --- | --- | --- | --- |
| Mean annual runoff (MAR) | (Million m3) | 32.26 | 32.37 |
| Standard deviation of annual flows (S) | (Million m3/yr) | 15.59 | 11.89 |
| Coefficient of variability (S/MAR) | (%) | 48.32 | 36.75 |
| Coefficient of skewness | - | 0.3693 | 0.1866 |
| Range | (% MAR) | 272.74 | 132.85 |
| Autocorrelation coefficient of annual flows | - | 0.3249 | -0.1567 |
| Mean of logs of annual flows | (Million m3) | 1.4537 | 1.4794 |
| Standard deviation of logs of annual flows | - | 0.2359 | 0.1727 |
| Index of seasonal variability | (%) | 22.12 | 22.01 |

## Observed versus simulated streamflow (monthly)

## Observed versus simulated streamflow (annual)

## Monthly streamflow histogram

## Observed versus simulated flow scatter diagram

## Monthly streamflow cumulative frequency curve

## Seasonality of flows

# Calibration at Gauge MG19

## Statistics of simulated and observed sequences

| Index | Unit | Observed | Simulated |
| --- | --- | --- | --- |
| Mean annual runoff (MAR) | (Million m3) | 32.23 | 30.32 |
| Standard deviation of annual flows (S) | (Million m3/yr) | 13.74 | 10.58 |
| Coefficient of variability (S/MAR) | (%) | 45.47 | 34.89 |
| Coefficient of skewness | - | 0.2727 | 0.0989 |
| Range | (% MAR) | 347.34 | 207.81 |
| Autocorrelation coefficient of annual flows | - | 0.3800 | 0.0542 |
| Mean of logs of annual flows | (Million m3) | 1.4239 | 1.4523 |
| Standard deviation of logs of annual flows | - | 0.2494 | 0.1698 |
| Index of seasonal variability | (%) | 23.41 | 23.87 |

## Observed versus simulated streamflow (monthly)

## Observed versus simulated streamflow (annual)

## Monthly streamflow histogram

## Observed versus simulated flow scatter diagram

## Monthly streamflow cumulative frequency curve

## Seasonality of flows

# Calibration at Gauge MG23

## Statistics of simulated and observed sequences

| Index | Unit | Observed | Simulated |
| --- | --- | --- | --- |
| Mean annual runoff (MAR) | (Million m3) | 389.67 | 388.27 |
| Standard deviation of annual flows (S) | (Million m3/yr) | 188.39 | 161.74 |
| Coefficient of variability (S/MAR) | (%) | 48.35 | 41.66 |
| Coefficient of skewness | - | 0.1717 | 0.3881 |
| Range | (% MAR) | 297.43 | 302.11 |
| Autocorrelation coefficient of annual flows | - | 0.2823 | 0.3812 |
| Mean of logs of annual flows | (Million m3) | 2.5338 | 2.5504 |
| Standard deviation of logs of annual flows | - | 0.2405 | 0.1951 |
| Index of seasonal variability | (%) | 23.12 | 23.61 |

## Observed versus simulated streamflow (monthly)

## Observed versus simulated streamflow (annual)

## Monthly streamflow histogram

## Observed versus simulated flow scatter diagram

## Monthly streamflow cumulative frequency curve

## Seasonality of flows