# Rainfall

## Overview

Rainfall data for the study area were acquired from the Ministry of Natural Resources (Department of Metrology) as well as the South African Weather Bureau.  There is a significant coverage of rainfall gauges, particularly around the border areas (as is shown in Figure A.4 in Annexure A), however, there is a scarcity of rainfall data in the interior of Lesotho.  In particular, the lack of rain gauges in the higher lying areas of the Study Area may lead to an under-estimation of catchment rainfall.

Rainfall data were required for two purposes in this assignment, namely for the simulation of catchment runoff using the WRSM 2000 model and for the simulation of rainfall on the surface of impoundments using the WRYM model.  The process of producing such rainfall data was as follows :

Preliminary screening and evaluation of rainfall data;

Grouping and patching of rain gauges;

Final screening and evaluation of rainfall data; and

Creation of catchment rainfall files.

The following sections discuss each of these steps in more detail.

## Preliminary screening

A preliminary evaluation of the rainfall data was undertaken and this screening exercise indicated that much of the rainfall data are poor and not fit for use in a hydrological study such as this.  Inspection of these data revealed that many of the rainfall records were neither long enough nor reliable enough to simulate streamflow.  In addition, the locations of many of the rain gauges are too remote to be representative of the rainfall at the various points of interest in the Study Area.  A total of 57 rain gauges were selected for use in the subsequent patching exercise, and 15 rain gauges were used for the streamflow generation.

Listings of the raw observed rainfall records of those gauges finally selected for streamflow simulation purposes are provided in Annexure B.  Part of the screening exercise was to generate cumulative mass plots of the annual rainfall totals to check for stationarity of the data.  The mass plots of the final selected gauges are provided in Annexure C.

## Patching

The rainfall records selected after preliminary screening were patched and extended to create complete monthly data sets from 1935 to 1999.  Ideally, a longer record would have been preferable, however, only a few of the observed records extended back to 1920 and patching with such a dearth of data would have created unreliable results.  In addition, the last two years of the records had to be discarded since the streamflow simulation model (WRSM2000) does not accept data after 1999 in the current format.  Rather than reformat the entire rainfall database, it was decided to utilise the slightly shorter records.  This still provides 65 years of records, which is deemed acceptable for stochastic streamflow modelling.

Table 2.1 presents the various groups of rain gauges that were used for the patching process.  The gauges indicated in bold are those that were eventually selected for use in this assignment.  Those rainfall records that were used for patching but that were not used in the assignment are fit for use but were considered to be too remote to be representative of the rainfall on the three catchments considered.  Listings of the patched rainfall records of those gauges used for streamflow generation are provided in Annexure D.

Table 2.1 : Grouping of rain gauges used for patching purposes.

| Group 1 | Group 2 | Group 3 | Group 4 | Group 5 | Group 6 | Group 7 |
| --- | --- | --- | --- | --- | --- | --- |
| 297-337 | 298-244 | 265-875 | 265-039 | 263-888 | 235-110 | 204-392 |
| 297-401 | 298-301 | 266-001 | 297-082 | 264-022 | 235-183 | 204-486 |
| 297-436 | 298-481 | 266-370 | 297-388 | 264-039 | 235-243 | 204-515 |
| 297-519 | 298-512 | 266-437 |  | 264-042 | 264-715 | 204-518 |
| 297-544 | 298-545 | 266-931 |  | 264-110 | 264-836 | 204-640 |
| 297-612 | 298-638 | 266-646 |  | 264-235 |  | 204-819 |
| 297-721 | 298-791 | 267-126 |  | 264-291 |  | 233-775 |
| 297-825 | 298-818 | 267-107 |  | 264-417 |  | 234-150 |
| 298-031 | 298-871 |  |  | 264-459 |  | 234-170 |
| 298-194 | 299-008 |  |  | 264-473 |  |  |
| 298-481 | 332-834 |  |  | 264-735 |  |  |

Note : Gauges in bold italics were those selected for streamflow generation.

## Final selection of rainfall gauges

The patched rainfall records for those gauges considered fit for use were then selected according to their geographical location relative to the catchments and their length of record.  Table 2.2 provides a list of the rain gauges that were eventually selected for the purposes of simulating catchment runoff.  The rainfall records were combined to generate the aerial rainfall over the three catchments of interest using the HDYP08 model.  Listings of the catchment rainfall files are provided in Annexure E.

Table 2.2 : Details of rain gauges used in this assignment.

| Gauge number | Gauge name | Start date | End date | Length of record (years) | Elevation (m.a.s.l.) | Latitude (S) | Longitude (E) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ngoajane/Hololo Catchment : |
| 297436 | Butha-Buthe | 1930 | 2002 | 72 | 1768 | 28º 46' | 28º 15' |
| 297612 | Hololo | 1964 | 2002 | 58 | 1640 | 28º 43' | 28º 21' |
| 297825 | St Peters | 1964 | 2002 | 58 | 1860 | 28º 45' | 28º 28' |
| 298194 | Ox Bow | 1957 | 2002 | 45 | 2591 | 28º 43' | 28º 37' |
| 298244 | Caledonia | 1921 | 1982 | 61 | 1951 | 28º 34' | 28º 39' |
| Hlotse Catchment : |
| 265875 | Pelaneng | 1932 | 1979 | 47 | 2040 | 29º 05' | 28º 30' |
| 266001 | Rampai | 1970 | 1995 | 25 | 2901 | 29º 01' | 28º 30' |
| 297082 | Leribe | 1930 | 2002 | 72 | 1666 | 28º 53' | 28º 03' |
| 297388 | Pitseng | 1937 | 2002 | 65 | 1780 | 28º 57' | 28º 13' |
| Makhaleng Catchment : |
| 233775 | Thabana Morena | 1936 | 2002 | 66 | 1676 | 29º 57' | 27º 25' |
| 234150 | Mpharane/Mt Carmel | 1925 | 2002 | 77 | 1752 | 30º00' | 27º 35' |
| 234170 | Malealea | 1954 | 2002 | 48 | 1966 | 29º 51' | 27º 34' |
| 264417 | Roma | 1935 | 2001 | 66 | 1646 | 29º 27' | 27º 44' |
| 264715 | Molimo Nthuse | 1962 | 2002 | 40 | 2040 | 29º 25' | 27º 54' |
| 264836 | Thaba Putsoa | 1962 | 2002 | 40 | 2600 | 29º 26' | 27º 58' |