## Slide 1
Tales Carvalho Resende
31 July 2015
Johannesburg, South Africa
Presentation of the Stampriet Transboundary Aquifer System assessment indicators
+
Adoption of workplan for follow-up

## Slide 2
GGRETA - Methodology
2
To simplify complex systems

## Slide 3
GGRETA - Methodology
3
Multi-disciplinary assessment:
  Hydrogeology
  Environmental & Socio-economic (incl. gender)
  Legal & Institutional (incl. gender)
Indicators based assessment
  Existing data
Target group for outputs is non-technical:
  Managers, Decision makers, Stakeholders incl. general Public

## Slide 4
GGRETA – Data to be collected
4
1. Data to be collected
2. Indicators calculated from data collected

## Slide 5
GGRETA – Data to be collected
5
Hydrogeology:
  A. Physiography and Climate
  Temperature, Precipitation, Evapo-trasnpiration, Land use, Topography and Surface water network
  B. Aquifer geometry
  Hydrogeological map, Geo-referenced boundary of the Transboundary Aquifer, Depth of water table/piezometric surface, Depth to top of aquifer formation, Vertical thickness of the aquifer, Degree of confinement, Aquifer's cross section
  C. Hydrogeological Characteristics
  Aquifer recharge, Aquifer lithology, Soil types, Porosity, Transmissivity and vertical connectivity, Total groundwater volume, Groundwater depletion, Natural discharge mechanism, Discharge by springs

## Slide 6
GGRETA – Data to be collected
6
Hydrogeology:
  A. Physiography and Climate
  Temperature, Precipitation, Evapo-trasnpiration, Land use, Topography and Surface water network
  B. Aquifer geometry
  Hydrogeological map, Geo-referenced boundary of the Transboundary Aquifer, Depth of water table/piezometric surface, Depth to top of aquifer formation, Vertical thickness of the aquifer, Degree of confinement, Aquifer's cross section
  C. Hydrogeological Characteristics
  Aquifer recharge, Aquifer lithology, Soil types, Porosity, Transmissivity and vertical connectivity, Total groundwater volume, Groundwater depletion, Natural discharge mechanism, Discharge by springs

## Slide 7
GGRETA – Data to be collected
7
Environmental & Socio-economic:
  D. Environmental
  Suitable for human consumption (natural groundwater quality), Groundwater pollution, Solid Waste and waste water control, Shallow groundwater table
  E. Socio-economic
  Population (total and density), Groundwater and Surface water use, Dependence of industry and agriculture on groundwater, Percentage of population covered by public water supply, Percentage of population covered by public sanitation

## Slide 8
GGRETA – Data to be collected
8
Legal & Institutional:
  F. Transboundary legal and institutional framework
  Agreement, treaty, MoU
  I. Domestic legal and institutional framework
  Ownership of groundwater, Water resources planning, Groundwater resources abstraction and use, Abatement and control of groundwater pollution, Water resources protection measures, Government and non-government (including informal) water institutions, Implementation, administration and enforcement of the legislation on the statute books

## Slide 9
GGRETA – Indicators
9
1. Data to be collected
2. Indicators calculated from data collected

## Slide 10
Indicators
10
1. Very low: < 2 mm/yr
2. Low: 2-20 mm/yr
3. Medium: 20-100 mm/yr
4. High: 100-300 mm/yr
5. Very high: > 300 mm/yr
1.1 Recharge
Rate
Indicator group 1: Defining or constraining the value of aquifers and their potential functions
Comments
No reliable recharge estimate is available for the confined aquifers, but it is very low (virtually non-renewable groundwater resources)

## Slide 11
11
Indicator group 1: Defining or constraining the value of aquifers and their potential functions
Comments
Very low recharge in combination with low population density
1.2 Renewable groundwater per capita
1. Low: < 1000 m3/yr/capita
2. Medium: 1000 – 5000 m3/yr/capita
3. High: > 5000 m3/yr/capita
Indicators

## Slide 12
12
Percentage of aquifer area with natural groundwater quality satisfying local drinking water standards.
1.3 Natural Background Quality
fresh
Saline Arsenic
fresh
1. Very low: < 20%
2. Low: 20 - 40%
3. Medium: 40-60%
4. High: 60-80%
5. Very high: > 80%
Indicator group 1: Defining or constraining the value of aquifers and their potential functions
Suitability for drinking water used as criterion.
It is accepted that local drinking water standards may vary.
Comments
Indicators

## Slide 13
13
Indicator group 1: Defining or constraining the value of aquifers and their potential functions
Comments
Proxy for the aquifer’s resilience to climatic variability
1.4 Aquifer buffering capacity
1. Low: < 10 years
2. Medium: 10 – 100 years
3. High: > 100 years
Ratio between volume stored and long-term mean ground­water recharge (equivalent to mean residence time)
Indicators

## Slide 14
14
Indicator group 1: Defining or constraining the value of aquifers and their potential functions
Comments
Auob/Nossob
Class 1 corresponds to ‘non-renewable groundwater’
1.5 Aquifer vulnerability to climate change
1. Low: confined aquifers containing only fossil water or receiving negligible recent recharge.
2. Medium: weakly recharged aquifers with limited interaction with other components of the hydrological cycle, due to location at considerable depth and/or hydraulic confinement.
3. High: aquifers actively interacting with streams, atmosphere
Extent of expected groundwater budget regime change in response to change in climatic conditions
Indicators

## Slide 15
15
Indicator group 1: Defining or constraining the value of aquifers and their potential functions
Comments
- Approximate criteria for “Moderately to highly vulnerable: “
> 0.3 in GOD method
> 100 in DRASTIC method
1.5 Aquifer vulnerability to pollution
1. Very low: < 20%
2. Low: 20 -40%
3. Medium: 40-60%
4. High: 60-80%
5. Very high: > 80%
Percentage of its horizontal area where the aquifer is considered moderately to highly vulnerable to pollution
Indicators

## Slide 16
16
Percentage of groundwater in total water abstraction for all human water uses
Groundwater
Lake water
River water
Groundwater
2.1 Human dependancy on groundwater
1. Very low: < 20%
2. Low: 20-40%
3. Medium: 40-60%
4. High: 60-80%
5. Very high: > 80%
Indicator group 2: Role and importance of groundwater for humans & environment
Abstraction of water includes the quantity used and all losses.
No data available, but there is no permanent surface water in the area.
Comments
Indicators

## Slide 17
17
Percentage of groundwater in total water abstraction for domestic use
Groundwater
Lake water
River water
Groundwater
2.2 Human dependency on groundwater for domestic water supply
1. Very low: < 20%
2. Low: 20-40%
3. Medium: 40-60%
4. High: 60-80%
5. Very high: > 80%
Indicator group 2: Role and importance of groundwater for humans & environment
Abstraction of water includes the quantity used and all losses.
Comments
Indicators

## Slide 18
18
Percentage of groundwater in total water abstraction for agricultural water supply
Groundwater
Lake water
River water
Groundwater
2.3 Human dependency on groundwater for agricultural water supply
1. Very low: < 20%
2. Low: 20-40%
3. Medium: 40-60%
4. High: 60-80%
5. Very high: > 80%
Indicator group 2: Role and importance of groundwater for humans & environment
Surface water contributes to livestock watering, in the form of water ponds
Comments
Indicators

## Slide 19
19
Percentage of groundwater in total water abstraction for industrial use
Groundwater
Lake water
River water
Groundwater
2.4 Human dependency on groundwater for industrial water supply
1. Very low: < 20%
2. Low: 20-40%
3. Medium: 40-60%
4. High: 60-80%
5. Very high: > 80%
Indicator group 2: Role and importance of groundwater for humans & environment
(Not applicable – apparently no industries in the area)
Comments
Indicators

## Slide 20
20
Percentage of the aquifer’s area where the aquifer has a phreatic water level shallower than 5 m below surface
Groundwater
Lake water
River water
Groundwater
2.5 Ecosystem dependency on groundwater
1. Very low: < 5%
2. Low: 5-10%
3. Medium: 10-25%
4. High: 25-50%
5. Very high: > 50%
Indicator group 2: Role and importance of groundwater for humans & environment
Auob/Nossob only
Phreatic water level taken as a proxy
Comments
Indicators

## Slide 21
21
Total annual groundwater discharge by springs, divided by mean annual groundwater recharge
Groundwater
Lake water
River water
Groundwater
2.6 Prevalence of springs
1. Very low: < 5%
2. Low: 5-10%
3. Medium: 10-25%
4. High: 25-50%
5. Very high: > 50%
Indicator group 2: Role and importance of groundwater for humans & environment
Springs are very sensitive for changes in groundwater budget. Therefore a meaningful indicator of change.
Comments
Indicators

## Slide 22
22
Observed polluted zones as percentage of total aquifer
3.1 Groundwater depletion
Indicator group 3: Changes in groundwater state
Comments
1. Absent to very low: < 2 mm/yr
2. Low: 2 -20 mm/yr
3. Medium: 20-50 mm/yr
4. High: 50-100 mm/yr
5. Very high: > 100 mm/yr
Depletion should target a long-year trend; short-term variations due to climatic variability should be discarded.
Indicators

## Slide 23
23
Observed polluted zones as percentage of total aquifer
3.2 Groundwater pollution
Indicator group 3: Changes in groundwater state
Local drinking water quality standards as a criterion.
Comments
1. Very low: < 5%
2. Low: 5-10%
3. Medium: 10-25%
4. High: 25-50%
5. Very high: > 50%
Indicators

## Slide 24
24
Number of people on top of aquifer per unit of area.
4.1 Population Density on Transboundary Aquifer
1. Very low: < 1 p/km2
2. Low: 1-10 p/km2
3. Medium: 10-100 p/km2
4. High: 100-1000 p/km2
5. Very high: > 1000 p/km2
Indicator group 4: Drivers of change and pressures
Indicators

## Slide 25
25
Total annual groundwater abstraction divided by long-term mean annual recharge.
1. Very low: < 2%
2. Low: 2-20%
3. Medium: 20-50%
4. High: 50-100%
5. Very high: > 100%
4.2 Grondwater Development Stress (=Abstraction/Recharge)
Indicator group 4: Drivers of change and pressures
Measure for the degree of modification of the groundwater budget (repercussions for outflow and storage)
Comments
Indicators

## Slide 26
26
Total annual groundwater abstraction divided by long-term mean annual recharge.
1. Very low: < 2%
2. Low: 2-20%
3. Medium: 20-50%
4. High: 50-100%
5. Very high: > 100%
4.2 Grondwater Development Stress (=Abstraction/Recharge)
Indicator group 4: Drivers of change and pressures
Measure for the degree of modification of the groundwater budget (repercussions for outflow and storage)
Comments
Indicators

## Slide 27
27
Adoption of workplan for follow-up
Activities | Time
Finalization of the final draft assessment report | End September 2015
Feedback from Governments | End of October 2015
2nd stakeholder consultation meeting (Stampriet) | Early November 2015
Finalization of final assessment report | November 2015
Final meeting (Paris?) | First half of December 2015

## Slide 28
THANK YOU
t.carvalho-resende@unesco.org