## Slide 1: UNESCO Stampriet TBA Project
Data Availability Report – 23 February 2014
by
Jürgen Kirchner

## Slide 2: Items will be discussed in the usual order
Physiography and Climate
Aquifer geometry
Hydrogeological characteristics
Environmental aspects and
Socio-economic aspects

## Slide 3: Physiography and Climate
A.1. Temperature
  Botswana: 1959-2012 Tshane & Tshabong [°C]
  Namibia: 6 Stations, varying periods between 1977 and 2014 from NOAA [°F]
  South Africa: Data available at SA Weather Service and Agricultural Research Council against cost.
Data appear to be available. It is suggested that long term mean minimum and maximum values from stations in and around the project area are combined in an xls or dbf file and then plotted on the TBA base map still to be prepared.

## Slide 4: Physiography and Climate
A.2. Precipitation
  Botswana: Data are available for 7 stations between 1970 (1979) to 2012 [mm]
  Namibia: 6 Stations, varying periods between 1977 and 2014 from NOAA [inches]
  South Africa: Data available at SA Weather Service and Agricultural Research Council against cost.
Annual rainfall data for a number of stations are available. mean annual precipitation data can be plotted on the TBA delineated map still to be prepared.

## Slide 5: Physiography and Climate
A.3. Evapotranspiration
  Botswana: Data for Tshane 1959-2009 and Tshabong 1959-2007 are available.
  Namibia: Namibia has only a map that shows the mean annual evaporation.
  South Africa: A spreadsheet with evaporation data from1961 to 1983 is available.
Compilation of a map showing the mean annual evaporation in steps of 200 mm is proposed.

## Slide 6: Physiography and Climate
A.4. Land use/Land cover
  Botswana: The intention is to digitize Google Earth maps.
  Namibia: A map of irrigation sites is available. Reference is made to the JICA report.
  South Africa: No such data have been collected.
Known land uses are Stock farming; Irrigation Nature conservation/Game parks/Tourism with possibly some Lodges which can be taken from maps. Lodge coordinates must be identified

## Slide 7: Physiography and Climate
A.5. Topography and Elevation
  Botswana: Shape files and maps are available
  Namibia: Maps and a digital elevation model is available
  South Africa: Data are available as shape files.
A digital elevation model for the whole TBA area can be produced from SRTM or ASTER data. Contour lines can also be created from these data.

## Slide 8: Physiography and Climate
A.6. Surface Water Networks
  Botswana: Rivers and pans are available as shape files
  Namibia: Rivers and pans are available as shape files
  South Africa: Rivers are available as shape files. Pans are assumed to be available.
A map of the surface water features (ephemeral rivers and pans) can be produced from the collected data and plotted on the TBA base map still to be prepared.

## Slide 9: Physiography and Climate
SUMMARISING
Although the respective xls files have still to be created no problems are foreseen to prepare tables and maps for
Temperature
Rainfall
Evaporation
Topography and Elevation and
Surface water networks can be produced
Data for the Land use map must be generated

## Slide 10: Aquifer Geometry
B.1. Hydrogeological map
  Botswana: 1:1 000 000 map is available
  Namibia: 1:1 000 000 map is available [tif & jpg]
  South Africa: 1:500 000 map is available
A map showing lithology and groundwater potential can be produced from the available data. While the Namibian map represents largely the properties of TBA aquifers (rock types and potential) the Botswana and South African maps depict largely the properties of the Kalahari aquifers. I assume that the Botswana Hydrogeological map reflects the Kalahari aquifer in the area of the TBA aquifer.

## Slide 11: Aquifer Geometry
B.2. Geo-referenced boundary of the TBA aquifer
  Botswana: Two delineation versions have been offered
  Namibia: Based on Google Earth & Miller 2008
  South Africa: Include outliers?
A decision must still be taken about the eastern boundary of the Botswana TBA area and the South African TBA boundary must be changed so that it meets the Namibian one about 20 km south of Mata Mata.

## Slide 12: Aquifer Geometry
B.3. Depth of water table/piezometric water level
  Botswana: There are maps in reports and hopefully DWA and GSD database data
  Namibia: Monitoring data are insufficient. 400 JICA data exist
  South Africa: Good Kalahari data exist – no TBA
One map each for Kalahari and TBA is needed. For parts of Botswana and for Namibia data are available. For South Africa probably only Kalahari data.

## Slide 13: Aquifer Geometry
B.4. Depth to top of aquifer formation
  Botswana: Report, BCR and probably database data are available
  Namibia: Miller, 2008 contains maps and sections
  South Africa: Good Kalahari data exist – some cross-sections showing Karoo were also provided by the specialist.
Cross-sections can be constructed. It will be difficult to compile a map as sufficiently deep boreholes with coordinates exist only in parts of Botswana and South Africa.

## Slide 14: Aquifer Geometry
B.5. Vertical thickness of aquifer
  Botswana: Information is available e.g. from the Matsheng report
  Namibia: Miller 2008 contains maps and cross-sections
  South Africa: Good information on the Kalahari exists, for TBA aquifers there are much less data.
From the above information cross-sections through the basin can be constructed. It appears unlikely that a map can be drawn showing the thickness of the TBA aquifer as boreholes (with coordinates) that have penetrated the Ecca aquifers are largely missing in parts of the Botswana and South African TBA catchment.

## Slide 15: Aquifer Geometry
B.6. Degree of confinement
  Botswana: G. Lentswe reckons he can extract the data from BCRs and the Matsheng report
  Namibia: Kalahari is unconfined, Auob and Nossob are confined to semi-confined in the Salt Block
  South Africa: Kalahari is unconfined, TBA is semi-confined
Degree of confinement is a qualitative statement which can be described rather than plotted on maps. The available information suffices.

## Slide 16: Aquifer Geometry
B.7. Representative cross-sections
The data needed for and the construction of cross-sections have already been discussed above under B.4. Depth to top of aquifer formation and B.5. Vertical thickness of the aquifer.

## Slide 17: Aquifer Geometry
summarising
A decision on the TBA delineation must be taken.
Hydrogeological maps are available but need to be harmonised.
Botswana has only boreholes in part of the catchment and in South Africa TBA information is scarce.

## Slide 18: Hydrogeological Characteristics
C.1. Aquifer Recharge
  Botswana: G. Lentswe reckons he can extract sufficient data from available reports.
  Namibia: Figures for various scenarios exist
  South Africa: Kalahari recharge values available
A reasonable estimate of the mean recharge of the Kalahari aquifers can be made. There is no recharge in the TransNossob. Considerable uncertainty remains regarding the mean recharge as individual events produce results varying by a factor of 102.

## Slide 19: Hydrogeological Characteristics
C.2. Aquifer Lithology
  Botswana: G. Lentswe listed the publications from which he can get the lithology.
  Namibia: L. Joel extracted from JICA & Miller 2008
  South Africa: L. Leshomo extracted from Haddon 2005
For Botswana the lithology of the different aquifers (Kalahari, Ntane and Otshe) still needs to be extracted from the literature. For the Namibian and South African aquifers it is available.

## Slide 20: Hydrogeological Characteristics
C.3. Soil types
  Botswana: A jpg image of soil and explanatory notes are available.
  Namibia: D. Muroua has compiled a soil map
  South Africa: A map showing Kalahari sand is attached to J. Leshomo’s report.
Maps from all three countries are available. The Botswana map needs to be digitised and all three maps must then be harmonised.

## Slide 21: Hydrogeological Characteristics
C.4. Porosity
  Botswana: G. Lentswe cites six publications that contain porosity information
  Namibia: No porosity values for the Kalahari exist. For the Auob values just over 20% were determined.
  South Africa: Currently there are no data on porosity.
Namibia has some values - further values for TBA aquifers can be found in pumping test data. While Botswana has still to extract data from literature, South Africa reports that so far there are no porosity data are available.

## Slide 22: Hydrogeological Characteristics
C.5. Transmissivity and vertical permeability
  Botswana: G. Lentswe cites six publications that contain porosity information
  Namibia: No porosity values for the Kalahari exist. For the Auob values just over 20% were determined.
  South Africa: Currently there are no data on porosity.
Namibia has some values - further values for TBA aquifers can be found in pumping test data. While Botswana has still to extract data from literature, South Africa reports that so far there are no porosity data are available.

## Slide 23: Hydrogeological Characteristics
C.6. Total Groundwater Volume
  Botswana: No data collected so far. In the Matsheng report there is a table with assumed reserves
  Namibia: There are insufficient data to describe this parameter for any of the 11 aquifers. Falke risked a trial.
  South Africa: van Wyk provided some estimates
Lentswe has not yet tried to calculate any storage values. Some values are in the Matsheng report. In Namibia one attempt has been made and in South Africa E. van Wyk has assessed the water stored in the Kalahari. The TBA figures are not regarded reliable. The stored water is not extractable because the Auob aquifer is collapsible.

## Slide 24: Hydrogeological Characteristics
C.7. Groundwater depletion
  Botswana: No data source identified so far
  Namibia: Sufficient long term water level graphs are not available
  South Africa: It is assumed that the Kalahari aquifer is under-utilised
Water-level monitoring records do not allow a definite statement whether the TBA aquifers are depleted. Preliminary indications are, however, that this is not the case.

## Slide 25: Hydrogeological Characteristics
C.8. Natural discharge mechanism
  Botswana: No data source identified so far
  Namibia: Evapotranspiration is the discharge mechanism in the Kalahari aquifer. At the lower end of the basin, groundwater flows out of the TBAs into the Kalahari
  South Africa: Evapo(trans)piration is the assumed discharge mechanism
For all aquifers the predominant discharge mechanism is evapotranspiration - for the TBA aquifers it is through seepage into the Kalahari aquifer.

## Slide 26: Hydrogeological Characteristcs
summarising
Some Botswana data still need to be extracted (Recharge, Lithology, Porosity, Transmissivity) and the TBA delineation must be decided on.
For porosity and transmissivity there are not sufficient data to construct a map.
Neither for the Kalahari nor for the TBA can a reliable value be given for the stored reserves. TBA stored resources can in any case not be abstracted.

## Slide 27: Environmental Aspects
D.1. Natural Groundwater quality
  Botswana: In general the groundwater quality is low
  Namibia: The water quality ranges from good to unsuitable. NSI data are questionable.
  South Africa: There are no springs in this area.
There is sufficient information to produce a groundwater quality map. For harmonisation the Standards (WHO or national) must be decided on. Main problems are TDS/EC, and Nitrate. In a few places Fluoride is even to high for animal consumption.

## Slide 28: Environmental Aspects
D.2. Pollution
  Botswana: Nitrate is the main pollutant
  Namibia: The water quality ranges from good to unsuitable. NSI data are questionable.
  South Africa: There are no springs in this area .
Although of local importance at places such as e.g. Hoachanas or Aminuis the yield of springs is so low that they do not play any role in the water balance of the Stampriet Artesian Basin. No springs have been reported from the Botswana and South African part of the Stampriet TBA.

## Slide 29: Environmental Aspects
D.3. Solid Waste and Waste Water Control
  Botswana: The specialist could not yet collect information
  Namibia: Information from the towns and settlements is collected.
  South Africa: Only the number of households that are served is recorded.
Field data for Botswana for Botswana have not been collected. Those for Namibia have been obtained for solid waste and were calculated for waste water. For South Africa these data were not recorded. It is suggested that the Botswana data are so that at least for these two countries harmonized reporting is possible.

## Slide 30: Environmental Aspects
D.4. Shallow water table
  Botswana: No such data were reported
  Namibia: There are only a few weak springs.
  South Africa: No such data were reported
Apart from a few comparatively weak springs shallow water exists at places in the Auob and Nossob River which support invasive alien Prosopis vegetation thereby supplanting the native acacia trees.

## Slide 31: Socio-economic Aspects
E.1. Population (total density)
  Botswana: Kalagadi North and South figures are available
  Namibia: The TBA is covered by parts of eight constituencies.
  South Africa: Data for the Mier Municipality are available only
Population figures are available in all three countries. The problem is that they have been collected for politically or administratively determined areas which do not coincide with the TBA delineation.

## Slide 32: Socio-economic Aspects
E.2. Groundwater use
  Botswana: Only groundwater is used but data are difficult to obtain
  Namibia: Water is used for human use; stock watering; and irrigation. Mostly indirect data will have to be used.
  South Africa: The DWA database is said to contain abstraction data.
The available information on groundwater use is incomplete. Figures are available for public water supply. Figures for non public water supply, e.g. use on farms for human use and stock watering can only be calculated based on number of persons and carrying capacity of the land. Namibian. Irrigation use could be approximated.

## Slide 33: Socio-economic Aspects
E.4. Dependence of Industry and Agriculture on groundwater
  Botswana: Preliminary results show the construction industry (brick moulding and building construction) and livestock watering to be the largest consumers
  Namibia: There are no industries in the aquifer area and the agricultural sector depends solely on groundwater.
  South Africa: Human consumption, stock watering. tourism and wildlife depend on groundwater.
It can be assumed that there is no surface water use of any practical importance.

## Slide 34: Socio-economic Aspects
E.6. Percentage of population covered by public sanitation
  Botswana: Type of toilet and number of household for each type are available.
  Namibia: Figures are available for whole constituencies
  South Africa: Percentage of households per toile type is available.
As for E.5. The data are available for administrative or politically demarcated areas and not for the Stampriet TBA delineated area.

## Slide 35: Socio-economic Aspects
summarising
The socio-economic data are generally available, however they refer to political or administratively demarcated areas, which makes it impossible to link these data to the Stampriet Transboundary Aquifer area.